## Slide 1: A Food-Energy-Water Calculator for Western Kansas
Mary C Hill (KU), Groundwater and uncertainty
Ruth Douglas Miller (KSU), Electrical energy
Danny Rogers (KSU), Agriculture
Joshua Roundy (KU), Climate, surface water, and drought indices

## Slide 2: What is a Food-Energy-Water Calculator?
Like a mortgage calculator but more complicated
Provides analysis of farm income tradeoffs
  Income increase from wind energy possible with changes to Kansas regulations
    Would allow more locally advantageous wind power development
  Income decrease because farmers would need to relinquish some water rights to get permission to develop wind energy in the more locally advantageous ways.
  The trade for water makes the change to Kansas regulations politically possible
Goals:
  Conserve and extend usable life of the Ogallala
  Maintain as much crop production into the future as possible
  Keep farmer revenues and local economies healthy by also harvesting wind energy

## Slide 3
KGS
The depleted aquifer region has some of the best wind in the country

## Slide 4: Turning to turbines: By Cole Epley / World-Herald staff writer (Omaho, NB)
Terry Brockhaus: “… land-lease payments of about $32,000 …”
  $5,000 to $7,000 per year per turbine
But later in the article…
Ed Woolsey: “One turbine has changed my life”
  What is happening here??
  Part is the Production Tax Credit (PTC). What else?
http://www.omaha.com/money/turning-to-turbines-as-commodity-prices-remain-low-wind-energy/article_2814e2cf-83a3-547d-a09e-f039e935f399.html
http://farmenergy.org/success-stories/wind-energy/new-crosswind-energy-project

## Slide 5
Special treatment of land owners/collectives who agree to water cutbacks for power sale rights.
  Sell electricity to coops without KCC “utility” label
  No generator size limit
  Coops can sign PPAs* with landowners
  Collectives are allowed.
  Multiple meters under one contract.
Grid capacity:
  Need lines and substations for MW-sized generators at landowner sites. Cost-share rules to pay for enhancements
  Coop role bigger?
*PPA, Power Purchase Agreement: agreed sale price, typically for 20 yrs
Necessary
Useful
Kansas changes needed to support more locally profitable wind development

## Slide 6: The calculator – initial design ideas
Equations, numbers, web links, web searches, judgement. User modification supported.
Users: define circumstances and preferences
Notes: The range of $70,000 annual income from wind power seems reasonable, and is consistent with the quote at the beginning of the talk about one turbine changing a farmer’s life.

## Slide 7
FAQs
Is local pumping enough to deplete the groundwater? Click here
What federal and state incentives are there for wind power development? Click here
1. Select your location and area
Results: Graph end year: 2072
558 acres
Wind and Solar Energy
Water
Climate
Key knowledge
3. Make Choices
2. Define Framework
Agri-culture
Select, then click here for defaults
Select to change. Select and click here to return to default
Consequences
Calculate
Plot Annual Average
Add Variability Add Uncertainty
2A
2B
2C
3A
3B
3C

## Slide 8
FAQs
Is local pumping enough to deplete the groundwater? Click here
What federal and state incentives are there for wind power development? Click here
1. Select your location and area
Results: Graph end year: 2072
558 acres
Wind and Solar Energy
Water
Climate
Key knowledge
3. Make Choices
2. Define Framework
Agri-culture
Select, then click here for defaults
Select to change. Select and click here to return to default
Consequences
Calculate
Plot Annual Average
Add Variability Add Uncertainty
Wind turbines Solar panels
Buy Lease Land Lease
Electric generation potential:
Wind speed map is HERE
Solar map is HERE
HPA map from KGS is HERE
Stories from your region are HERE
Field Crops Ranching
.
Choose via Crop Water Allocation CWA
from KSU
OR
Irrigation: Fresh Groundwater
Use county defaults for crops, water, fertilize, prices, etc.
3A
3B
3C

## Slide 9
FAQs
Is local pumping enough to deplete the groundwater? Click here
What federal and state incentives are there for wind power development? Click here
1. Select your location and area
Results: Graph end year: 2072
558 acres
Wind and Solar Energy
Water
Climate
Key knowledge
3. Make Choices
2. Define Framework
Agri-culture
Select, then click here for defaults
Select to change. Select and click here to return to default
Consequences
Calculate
Plot Annual Average
Add Variability Add Uncertainty
Wind turbines Solar panels
Buy Lease Land Lease
Electric generation potential:
Wind speed map is HERE
Solar map is HERE
Wind turbines 2 2 MW
Loan: 20 years APR 4%
Grid connection needed
HPA map from KGS is HERE
Stories from your region are HERE
Field Crops Ranching
.
Subsidies, insurance Options
Phase in period for irrigation change: 5 years
First year: 2017
Average past annual farm income: $32,000
Choose via Crop Water Allocation CWA
from KSU
OR
Irrigation: Fresh Groundwater
Reduce irrigation by 25% of 5 year average.
Years to no or little irrigation?
Calculate
Soil condition? Poor
Use county defaults for crops, water, fertilize, prices, etc.

## Slide 10
FAQs
Is local pumping enough to deplete the groundwater? Click here
What federal and state incentives are there for wind power development? Click here
1. Select your location and area
Results: Graph end year: 2072
558 acres
Wind and Solar Energy
Water
Climate
Key knowledge
3. Make Choices
Assume: average change temp +2º F , precip +0% to 2050. Precipitation probability scenario (DPS) A.
If temperature increases, precipitation must increase for the same drought probabilities to occur.
2. Define Framework
Wind turbines Solar panels
Buy Lease Land Lease
Electric generation potential:
Wind speed map is HERE
Solar map is HERE
Wind turbines 2 2 MW
Loan: 20 years APR 4%
Grid connection needed
$3M/turbine = $6M Life 20 yrs
Grid connection: $400,000/turbine
O&M: $31,000/yr/MW=$124,000/yr Electric price: $.038/kwh.
Factors: Grid 100% Production 45%
HPA map from KGS is HERE
Stories from your region are HERE
Field Crops Ranching
.
Agri-culture
Subsidies, insurance Options
Phase in period for irrigation change: 5 years
First year: 2017
Average past annual farm income: $32,000
Choose via Crop Water Allocation CWA
from KSU
OR
Select, then click here for defaults
Select to change. Select and click here to return to default
Irrigation: Fresh Groundwater
Precipitation 14” per year
At present pumping rates, dryland farming dominates in 2054. Map
Years added per area-wide 25% pumpage reduction: 5-10
Reduce irrigation by 25% of 5 year average.
Years to no or little irrigation?
Calculate
Soil condition? Poor
Consequences
Calculate
Plot Annual Average
Add Variability Add Uncertainty
Use county defaults for crops, water, fertilize, prices, etc.

## Slide 11
FAQs
Is local pumping enough to deplete the groundwater? Click here
What federal and state incentives are there for wind power development? Click here
1. Select your location and area
Results: Graph end year: 2072
558 acres
Wind and Solar Energy
Water
Climate
Key knowledge
3. Make Choices
Assume: average change temp +2º F , precip +0% to 2050. Precipitation probability scenario (DPS) A.
If temperature increases, precipitation must increase for the same drought probabilities to occur.
2. Define Framework
Wind turbines Solar panels
Buy Lease Land Lease
Electric generation potential:
Wind speed map is HERE
Solar map is HERE
Wind turbines 2 2 MW
Loan: 20 years APR 4%
Grid connection needed
$3M/turbine = $6M Life 20 yrs
Grid connection: $400,000/turbine
O&M: $31,000/yr/MW=$124,000/yr Electric price: $.038/kwh.
Factors: Grid 100% Production 45%
Added annual income= $67,184
Income: 4MW x 365 x 24 hours/year x 45% x $.038/kwh x 1000kw/Mw = $599,184.
Expenses: O&M $124,000 +
loan payment $408,000 = $532,000
HPA map from KGS is HERE
Stories from your region are HERE
Dryland farming delayed by 5-10 years. Use 7 years. Approximate year to start dryland farming is 2061
Field Crops Ranching
.
Agri-culture
Subsidies, insurance Options
Phase in period for irrigation change: 5 years
First year: 2017
Average past annual farm income: $32,000
Average annual income reduction after water use change implemented: 20%
(0%=no change), to $200,000.
Choose via Crop Water Allocation CWA
from KSU
OR
Select, then click here for defaults
Select to change. Select and click here to return to default
Irrigation: Fresh Groundwater
Precipitation 14” per year
At present pumping rates, dryland farming dominates in 2054. Map
Years added per area-wide 25% pumpage reduction: 5-10
Reduce irrigation by 25% of 5 year average.
Years to no or little irrigation?
Calculate
Soil condition? Poor
Consequences
Calculate
Plot Annual Average
Add Variability Add Uncertainty
Use county defaults for crops, water, fertilize, prices, etc.

## Slide 12: Intended uses of the Food-Energy-Water Calculator
Provides Kansas- and site-specific information to consider choices
  Approximates future income
Interested in considering turbine ownership??
  Work with legislators, electric coops, IOUs, vendors and banks to figure out how to realize the opportunities.
  To get started, see Windustry, or
  http://windlibrary.org/exhibits/show/business-models/introduction OR http://farmenergy.org/success-stories/wind-energy/new-crosswind-energy-project

## Slide 13: This is the first step
We are interested in your thoughts.
We hope for a continuing conversation.
We hope to develop workflows and software that can be used to address other issues elsewhere, such as
  Quantify pollutant budgets like nitrates, and other things like food
  Include stakeholder contributions – a FaceBook-like extension based on a shared issue of interest

## Slide 14
Questions?
Kansas: Feeding the World.
Powering the Nation?

## Slide 15: The following are slides for anticipated questions

## Slide 16: Sales from owned turbines - Illustrated
A Net metering
B Parallel Generation
C Commercial scale
Retail
Wholesale
Notes:   100kW in KS; up to 500kW elsewhere.
  1 month in KS; up to a year elsewhere (much more advantageous).
Net metering. Buy=sell price. Limit capacity and trading time
  100kW in KS
  1 month in KS
Parallel generation. Sell price = 150% of wholesale, figured instantly. Limit capacity. In KS:
  25 kW for residential customers, 200 kW for commercial customers
  Not more than 4% of utility peak demand
Community Wind (Windustry.org) Buy retail. Sell wholesale.
  No limits on capacity
  May allow aggregation of different energy capacity sources

## Slide 17: Sales from owned turbines - Illustrated
Retail
Wholesale
X
A Net metering
B Parallel Generation
C Commercial scale
Notes:   100kW in KS; up to 500kW elsewhere.
  1 month in KS; up to a year elsewhere (much more advantageous).
Net metering. Buy=sell price. Limit capacity and trading time
  100kW in KS
  1 month in KS
Parallel generation. Sell price = 150% of wholesale, figured instantly. Limit capacity. In KS:
  25 kW for residential customers, 200 kW for commercial customers
  Not more than 4% of utility peak demand
Community Wind (Windustry.org) Buy retail. Sell wholesale.
  No limits on capacity
  May allow aggregation of different energy capacity sources

## Slide 18: Sales from owned turbines - Illustrated
Retail
Wholesale
X
=
X
0.45
Production Factor
A Net metering
B Parallel Generation
C Commercial scale
Explains “One turbine has changed my life”
Notes:   100kW in KS; up to 500kW elsewhere.
  1 month in KS; up to a year elsewhere (much more advantageous).
Net metering. Buy=sell price. Limit capacity and trading time
  100kW in KS
  1 month in KS
Parallel generation. Sell price = 150% of wholesale, figured instantly. Limit capacity. In KS:
  25 kW for residential customers, 200 kW for commercial customers
  Not more than 4% of utility peak demand
Community Wind (Windustry.org) Buy retail. Sell wholesale.
  No limits on capacity
  May allow aggregation of different energy capacity sources

## Slide 19: Sales from owned turbines - Illustrated
Retail
Wholesale
X
X
0.45
Production Factor
There are also restrictions relating to timing and percent of utility peak demand.
A Net metering
B Parallel Generation
C Commercial scale
=
IOUs only in Kansas
Always limited, but very limited in Kansas
IOU: Investor Operated Utility, like Westar. KCC defines what is an IOU and thus who can own large wind generators in Kansas
Notes:   100kW in KS; up to 500kW elsewhere.
  1 month in KS; up to a year elsewhere (much more advantageous).
Net metering. Buy=sell price. Limit capacity and trading time
  100kW in KS
  1 month in KS
Parallel generation. Sell price = 150% of wholesale, figured instantly. Limit capacity. In KS:
  25 kW for residential customers, 200 kW for commercial customers
  Not more than 4% of utility peak demand
Community Wind (Windustry.org) Buy retail. Sell wholesale.
  No limits on capacity
  May allow aggregation of different energy capacity sources

## Slide 20: Sales from owned turbines - Illustrated
Retail
Wholesale
X
IOUs only in Kansas
X
0.45
Production Factor
Additional factors: Restrictions relating to timing and percent of utility peak demand.
In all cases, Kansas restrictions mean less money for private land owners than in many other states.
Always limited, but very limited in Kansas
A Net metering
B Parallel Generation
C Commercial scale
IOU: Investor Operated Utility, like Westar. KCC defines what is an IOU and thus who can own large wind generators in Kansas
=
Notes:   100kW in KS; up to 500kW elsewhere.
  1 month in KS; up to a year elsewhere (much more advantageous).
Net metering. Buy=sell price. Limit capacity and trading time
  100kW in KS
  1 month in KS
Parallel generation. Sell price = 150% of wholesale, figured instantly. Limit capacity. In KS:
  25 kW for residential customers, 200 kW for commercial customers
  Not more than 4% of utility peak demand
Community Wind (Windustry.org) Buy retail. Sell wholesale.
  No limits on capacity
  May allow aggregation of different energy capacity sources

## Slide 21
Farm net income = 5**
From agriculture
Electric meter
Farm Net Income Cartoon
Water well
**Approximate relative values
Agricultural production
Electric use
Notes: From Ruth on v0:
SPP does not generate or sell electricity. It is a regulatory agency, it only controls who may sell to whom (among utilities; nothing to do with retail) at what price in real time, and a lot of the time it doesn't do much. Change the slides to this:
replace "SPP" with "Electricity Generation: IOU or Coop" (IOU = Investor-owned utility--in KS = Westar. Generation Coop in KS = Sunflower Electric)
Adding wind turbine &/or solar panel symbols to the circles in 6-8 would also help explain the idea.
Title page looks fine for my part. If you want to clarify things a bit more you might say "Electricity" or "Electric energy" instead of just "energy"; lots of people in KS think oil/gas when you say "energy.“
Via web: 126 acres per center pivot irrigation. 124 acres per wind turbine for turbines in an array

## Slide 22
Electric meter
Water well
Farm net income = 3
From agriculture
Farm Net Income Cartoon
Still important to keep this land producing agricultural goods for the country.
Agricultural production
Electric use

## Slide 23
Electric meter
Water well
Farm net income = 3 + 0.5
From agriculture and land lease
Wind Energy Land lease agreement
No investment by the land owner
2 MW wind turbine
Farm Net Income Cartoon
Agricultural production
Electricity production
Electric use
Notes: IOU, like

## Slide 24
Electric meter
Water well
Farm net income = 3 + ???
From agriculture and turbine
Agricultural production
Electricity production
2 MW wind turbine
Wind Energy Ownership
Investment by the land owner
Farm Net Income Cartoon
Electric use
Notes: VA limit is 500kw

## Slide 25
Electric meter
Water well
Farm net income = 3 + 6
From agriculture and turbine
Agricultural production
Electricity production
2 MW wind turbine
Wind Energy Ownership
More complicated arrangement
Farm Net Income Cartoon
Electric use
Notes: VA limit is 500kw

## Slide 26
Special treatment of land owners/collectives who agree to water cutbacks for power sale rights.
  Sell electricity to coops without KCC “utility” label
  No generator size limit
  Coops can sign PPAs* with landowners
  Collectives are allowed.
  Multiple meters under one contract.
Grid capacity:
  Need lines and substations for MW-sized generators at landowner sites. Cost-share rules to pay for enhancements
  Coop role bigger?
*PPA, Power Purchase Agreement: agreed sale price, typically for 20 yrs
Necessary
Useful
Kansas changes needed to support more locally profitable wind development

## Slide 27: Relate irrigation to ag production and income
For long forecasts include aquifer projections from KGS groundwater models
2 2MW wind turbines
Added annual income= $67,184
vs ~$12,000 for land lease
Income:
4MW x 365x24 hours/year x
45% x Production factor
$.038/kwh x Price for electricity
1000kw/Mw =
$599,184 Total
Expenses:
O&M $124,000 +
loan payment $408,000 Total
Calculate income from electrical generation

## Slide 28
Wind and Solar Energy
Water
Climate
Key knowledge
3. Make Choices
Consequences
2. Define Framework
Agri-culture
FAQs
1. Select your location and area
Select, then click here for defaults
Graph end year: 2050
Click for default

## Slide 29
Wind and Solar Energy
Water
Climate
Key knowledge
3. Make Choices
Consequences
2. Define Framework
Wind turbines Solar panels
Buy Lease Rent land
Electric generation potential:
Wind speed map is HERE
Solar map is HERE
HPA map from KGS is HERE
Stories from your region are HERE
Field Crops
Ranching
Use county defaults for crops, water, fertilize, prices, etc.
Agri-culture
FAQs
Is it local pumping that is depleting the groundwater? Click here
How does weather variability affect agricultural income? Click here
1. Select your location and area
Choose via Crop Water Allocation from KSU CWA
OR
Select, then click here for defaults
Graph end year: 2050
Click for default
558 acres
Irrigation: Fresh Groundwater

## Slide 30
Wind and Solar Energy
Water
Climate
Key knowledge
3. Make Choices
Consequences
2. Define Framework
Wind turbines Solar panels
Buy Lease Rent land
Electric generation potential:
Wind speed map is HERE
Solar map is HERE
Wind turbines 2 2 MW @.
Loan: 20 years APR 4%
Grid connection needed
HPA map from KGS is HERE
Stories from your region are HERE
Field Crops
Ranching
Use county defaults for crops, water, fertilize, prices, etc.
Agri-culture
Subsidies, insurance Options
Phase in period for irrigation change: 5 years
First year: 2017
Average past annual farm income: $32,000
FAQs
Is it local pumping that is depleting the groundwater? Click here
How does weather variability affect agricultural income? Click here
1. Select your location and area
Choose via Crop Water Allocation from KSU CWA
OR
Select, then click here for defaults
Graph end year: 2050
Click for default
558 acres
Reduce irrigation by 25% of 5 year average.
Years to unable to irrigate?
Calculate
Soil condition? Poor
Irrigation: Fresh Groundwater

## Slide 31
Wind and Solar Energy
Water
Climate
Key knowledge
3. Make Choices
Consequences
Assume: average change temp +2º F , precip +0% to 2080. Drought probability scenario (DPS) A. If temperature increases, precipitation must increase to see the same drought probabilities.
2. Define Framework
Wind turbines Solar panels
Buy Lease Rent land
Electric generation potential:
Wind speed map is HERE
Solar map is HERE
Wind turbines 2 2 MW @.
Loan: 20 years APR 4%
Grid connection needed
$3M/turbine = $6M Life 20 yrs
Grid connection: $400,000/turbine
O&M: $31,000/yr/MW=$124,000 Electric price: $.038/KWH.
Factors: Grid 100% Production 45%
HPA map from KGS is HERE
Stories from your region are HERE
Field Crops
Ranching
Use county defaults for crops, water, fertilize, prices, etc.
Agri-culture
Reduced crop production caused by reduced irrigation (0%=no change)
Year: Average Drought
Crops 10% 90%
Livestock 15% 95%
Probability 50% 5%
Subsidies, insurance Options
Phase in period for irrigation change: 5 years
First year: 2017
Average past annual farm income: $32,000
FAQs
Is it local pumping that is depleting the groundwater? Click here
How does weather variability affect agricultural income? Click here
1. Select your location and area
Choose via Crop Water Allocation from KSU CWA
OR
Based on location and DPS from climate
Select, then click here for defaults
Graph end year: 2050
Click for default
Precipitation 14” per year
Time to dry farming at historic pumping rates: 2054. See map
Years added per area-wide 25% pumpage reduction: 5-10
558 acres
Irrigation: Fresh Groundwater
Reduce irrigation by 25% of 5 year average.
Years to unable to irrigate?
Calculate
Soil condition? Poor

## Slide 32
Wind and Solar Energy
Water
Climate
Key knowledge
3. Make Choices
Consequences
Assume: average change temp +2º F , precip +0% to 2080. Drought probability scenario (DPS) A. If temperature increases, precipitation must increase to see the same drought probabilities.
2. Define Framework
Wind turbines Solar panels
Buy Lease Rent land
Electric generation potential:
Wind speed map is HERE
Solar map is HERE
Wind turbines 2 2 MW @.
Loan: 20 years APR 4%
Grid connection needed
$3M/turbine = $6M Life 20 yrs
Grid connection: $400,000/turbine
O&M: $31,000/yr/MW=$124,000 Electric price: $.038/KWH.
Factors: Grid 100% Production 45%
Added annual income= $67,184
Income: 4MW x 365x24 hours/year x 45% x $.038/kwh x 1000kw/Mw = $599,184.
Expenses: O&M $124,000 +
loan payment $408,000
HPA map from KGS is HERE
Stories from your region are HERE
Dryland farming delayed by 5-10 years. Use 7 years. Approximate year to start non-irrigated farming is 2061
Field Crops
Ranching
Use county defaults for crops, water, fertilize, prices, etc.
Agri-culture
Reduced crop production caused by reduced irrigation (0%=no change)
Year: Average Drought
Crops 10% 90%
Livestock 15% 95%
Probability 50% 5%
Subsidies, insurance Options
Phase in period for irrigation change: 5 years
First year: 2017
Average past annual farm income: $32,000
Average annual income reduction after water use change implemented: 25%
(0%=no change), to $24,000.
FAQs
Is it local pumping that is depleting the groundwater? Click here
How does weather variability affect agricultural income? Click here
1. Select your location and area
Choose via Crop Water Allocation from KSU CWA
OR
Based on location and DPS from climate
Select, then click here for defaults
Graph end year: 2050
Click for default
558 acres
Irrigation: Fresh Groundwater
Precipitation 14” per year
Time to dry farming at historic pumping rates: 2054. See map
Years added per area-wide 25% pumpage reduction: 5-10
Reduce irrigation by 25% of 5 year average.
Years to unable to irrigate?
Calculate
Soil condition? Poor

## Slide 33
Distribution
Electric meter
Water well
Trans-mission
Farm net income = 3 + 0.5
From agriculture and land lease
IOU or Coop
Electricity
Wind Energy Land lease agreement
No investment by the land owner
2 MW wind turbine
Farm Net Income Cartoon
Investor Owned Utilities (IOUs, like Westar)
and Coops (like Sunflower)
Agricultural production
Electricity production
Notes: IOU, like